IOP-GANFO-242401014

2.4GHz 24dBi Grid Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400MHz – 2483MHz |
| Gain | 24 dBi |
| VSWR | 1.5 : 1 Max. |
| Polarization | Horizontal, Vertical |
| HPBW / Horizontal | 10° |
| HPBW / Vertical | 14° |
| Front to back ratio | 31dB |
| Power handing | 100W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 234Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gray |
| Radome material | UV resistant , Aluminum Die Cast |
| Weight | 3.6Kg |
| Dimensions | 60 x 90 cm |
| Mast Diameter | Φ 4 – 5 cm |