IOP-PANFO-581801818

5GHz 18dBi Panel Antenna

| Electrical Specification |
| --- |
| Frequency range | 5250MHz – 5875MHz |
| Gain | 18 dBi |
| VSWR | 2 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 18° Max |
| HPBW / Vertical | 18° Max |
| Front to back radio | 25dB |
| Power handing | 10W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gary - white |
| Radome material | ABS,UV resistant |
| Weight | 825g |
| Dimensions | 215 × 200 × 50 mm |