IOP-YANFO-581403025

5GHz 14dBi Yagi Antenna

| Electrical Specification |
| --- |
| Frequency range | 5725MHz – 5875MHz |
| Gain | 14 dBi |
| VSWR | 2 : 1 Max. |
| Polarization | Linear, Vertical |
| HPBW / Horizontal | 30° |
| HPBW / Vertical | 25° |
| Power handing | 5W (cw) |
| Impedance | 50 Ohms |
| Connector | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +80℃ |
| Humidity | 95% @ 55℃ |
| Radome color | Gary |
| Radome material | ABS, UV resistant |
| Weight | 305g |
| Mechanical tile | +10 ~ -15° |
| Dimensions | 320 × 89 × 50 mm |