IOP-OANFO-DB0536035

2.4 & 5GHz 3 & 5dBi Dual Band Omni Antenna

| Electrical Specification |
| --- |
| Frequency range | 2400 – 2500MHz | 5150 – 5900MHz |
| Peak gain | 4 dBi | 7 ~ 8 dBi |
| Average gain | 3 dBi | 4.5 ~ 5.5 dBi |
| VSWR | 2 : 1 Max. | 2 : 1 Max. |
| Polarization | Linear, Vertical | Linear, Vertical |
| HPBW / Horizontal | 360° | 360° |
| HPBW / Vertical | 35° | 20° |
| Power handing | 10W (cw) | 10W (cw) |
| Impedance | 50 Ohms | 50 Ohms |
| Connector | N Jack | N Jack |
| Environmental & Mechanical Characteristics |
| Survival wind speed | 216Km/hr |
| Temperature | -40℃ to +70℃ |
| Humidity | 95% @ 55℃ |
| Radome color | White |
| Radome material | ABS, UV resistant |
| Weight | 206g |
| Dimensions | Φ20 × 260 mm |